entity debouncing is
  generic( COUNT_MAX: integer := 255;
        COUNT_WIDTH: integer := 8);
 port( clk in std_logic;
       I in std_logic;
       O out std_logic);
end debouncing;

architecture behave of debouncing is

signal count: std_logic_vector(COUNT_WIDTH-1 down 0);
signal Iv: std_logic := ´0´;
begin
 process(clk)
   if (clk´event and clk = ´1´) then
       if ( I = Iv) then
        if (count = COUNT_MAX) then
        O <= I;
        else
        count <= count +1;
        end if;
        else
        count <= 0;
        Iv <= I;
       end if;
  end process;

end behave;

—-module debouncer(
—- input clk,
—- input I,
—- output reg O
—- );
—- parameter COUNT_MAX=255, COUNT_WIDTH=8;
—- reg [COUNT_WIDTH-1:0] count;
—- reg Iv=0;
—- always@(posedge clk)
—- if (I == Iv) begin
—- if (count == COUNT_MAX)
—- O <= I;
—- else
—- count <= count + 1'b1;
—- end else begin
—- count <= 'b0;
—- Iv <= I;
—- end

—-endmodule